## Slide 1: ERAU ASCEND! OverView
Adam Ritchie
Nicholas Hammons
Andrew Grant
Geimi Delarge

## Slide 2: Overview
Flight Objectives
Payload
Flights Taken
Conclusions
Future Goals

## Slide 3: Flight Objectives
Gain better knowledge of the nature of composite materials
Gather temperature data along the flight
Gather IMU data
Gather pressure data along the flight
Gather solar cell data along the flight
Track and recover payload

## Slide 4: Payload
8 Inch Composite Cube
  Bi-directional Carbon with ¼” foam core
  E-glass shelving system and lid
Automatic Position Reporting System (APRS)
  Lassen IQ GPS
  TTY TinyTrak4 TNC
  Alinco radio
Logomatic Data Logger

## Slide 5: Payload (continued)
First Flight Only
  Sparkfun 6 DOF IMU
  HOBO Datalogger
Second Flight Only
  Invensys Pressure Sensor
  Dallas One Wire Thermistors
  Two Solar Cells
  28-X1 Picaxe Microcontroller

## Slide 6: Flight #1: Nov. 22, 2008
Launched from Gila Bend
Traveled 61.1 statute miles
Flight time: 2:02:32
Peak Altitude: 95,867 ft.
Landed south of Chandler
Source: kd7lmo.net

## Slide 7: Flight #1 (continued)
HOBO datalogger recorded temperature and relative humidity
IMU data was retrieved but could not be analyzed
GPS tracking was successful up to burst and then during part of the descent
Source: kd7lmo.net

## Slide 8: Flight #2: April 4, 2009
Launched from Gila Bend
Traveled 81.4 statute miles
Flight time: 1:57:05
Peak Altitude: 89,676 ft.
Landed East of Florence

## Slide 9: Flight #2 (continued)
Temperature, pressure, and solar cell data successfully recorded
GPS never acquired satellites due to antenna installation
Source: kd7lmo.net

## Slide 10: Conclusions
Two successful launches
  Recovered payload after both launches
  Gathered temperature, pressure, and IMU data
  Cannot put aluminum tape over GPS antenna
Created own systems instead of using heavy, off the shelf systems
Improved structural layout to improve wiring layout

## Slide 11: Future Goals
Reduce weight
Improve wiring by integrating PCB
Make GPS more reliable
Integrate solar cells to power the payload
Questions?

## Slide 12: Thank You!
Dr. Ron Madler
Jack Crabtree
Dr. John Nafziger
Chris Smith
ANSR
Susan Brew

## Slide 13: Structures and System Integration
Nicholas Hammons